Tracking
- Input: images and PairYolo
- Output: KeyFrames
- Initializes the map
- Track where each frame in the map
- Addes KeyFrames to LocalMapping

---
Tracking
Calls to MapPublisher every time new map is made

---
MapPublisher
- Input: pointer to Map, amount of Red and Blue cones
- Output: 2D maps of Red and Blue cones (ROS)
- Takes all 3D cone points and arrange in 2 Matrices for each color.
- Publish to ROS for more processing.

---
Frame
Gets an image
Extract ORB features
Arrange the ORB features in a cell grid for fast comparison.
Make KeyPoints out of ORB features.
Calculates frame position in the map (pose and orientation).

---
Frame addition
(For monocular) after finding KeyPoints in frame, assign KeyPoints for corresponding YOLO bounding boxes (AssignKPToYOLO):
Check which cells bounding box occuppies
Check if KeyPoints in these cells are in the bounding box
If so: add the type of the cone to a vector that classify the KeyPoints

---
LocalMapping
Makes the map:
Inserts KeyFrames.
Adds new MapPoints based on ORB features from new KeyFrames.
Remove redundent MapPoints and KeyFrames.

---
LocalMapping
- If one of the features that the MapPoint based on is cone, mark the MapPoint as cone.
- If a MapPoint is suspected to be a cone, dont remove.

---
Map
The database of ORBSLAM- contains all the MapPoints and KeyFrames.

---
Map
- Added a Set of MapPoints that is suspected to be Cones (in culling cone MapPoint is erased from the set)
- Added method that returns that set.

---
Planned
- Move the PairYolo creation to frame creation, instead of giving the SLAM class the pair.
- Add next layer that runs DBScan on the map. Will get the map through ros