## Slide 1
Introduction
Formula Student Germany 2020 will accept only driverless cars
A simple modular autonomous system is needed
  Localization and mapping
  Route planning
  Control
Goals
Localize the car in a track consisting of cones using camera only
Send location and map to route planning
Present a demo of a working system at EcoMotion 2019
ORB-SLAM is a general system that can't track specific objects
Needs to train the CNN with labeled data
Time restriction (for EcoMotion demo)
Challenges
DBSCAN
Camera
Results
Conclusions
Open source is amazing- cone_slam wouldn’t be possible in such a time scale without it
For the race in 2020 more advanced system is needed- several sensors fusion, maybe add lidar based slam as backup
ORB-SLAM
Spatial clustering
Input- Point cloud
Output- Clusters
cone_slam
SLAM for Driverless Formula
Tom Norman, Supervised by Vadim Indelman
ROS
    Modular system to transfer data between programs
    Has sophisticated visualization tools (good for debugging)
    Open source
YOLO
Visual SLAM
Input- Image
Output- Location
Open source and well established
Works with monocular and stereo
Works well on big scenarios
ZED Mini
  Stereo and Monocular options
  Has ROS wrapper
  Cheap
DBSCAN output on real scenario
The demo was a success- the car tracked the cones and planned a route between them
Stereo capabilities were added
September 2019
Implementation
Mapping and Localization:
  When creating frame in ORB-SLAM:
    Get bounding boxes and corresponding classes (blue or yellow cone) from YOLO
    Classify all ORB features in bounding box as corresponding class
  When creating map point in ORB-SLAM:
    If made of blue or yellow ORB feature- classify as such
  Send the point cloud created for clustering
Clustering:
  Run DBSCAN on received point cloud to get a map of cones
  Send given map forward for route planning
ORB-SLAM output on real scenario
YOLO output
Real time classification CNN
Input- Image
Output- bounding boxes and classes
Training data- 1300 hand labeled images of cones
cone_slam nodes and topics
cone_slam in action